## Slide 1: A Case for Subarray-Level Parallelism (SALP) in DRAM
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, Onur Mutlu

## Slide 2: Executive Summary
Problem: Requests to same DRAM bank are serialized
Our Goal: Parallelize requests to same DRAM bank at a low cost
Observation: A bank consists of subarrays that occassionally share global structures
Solution: Increase independence of subarrays to enable parallel operation
Result: Significantly higher performance and energy-efficiency at low cost (+0.15% area)

## Slide 3: Outline
Motivation & Key Idea
Background
Mechanism
Related Works
Results

## Slide 4: Introduction
Bank
DRAM
Bank
Bank
Bank
Req
Req
Req
Req
Req
Req
Req
Req
Bank conflict!
4x latency

## Slide 5: Bank conflicts degrade performance
Three Problems
  Requests are serialized
  Serialization is worse after write requests
  Thrashing in row-buffer
Row
Row
Row
Row
Bank
Row-Buffer
Req
Req
Req
Thrashing: increases latency

## Slide 6: Case Study: Timeline
time
Wr
Rd
Wr
Rd
time
Bank
time
Bank
Bank
Case #1. Different Banks
Case #2. Same Bank
1. Serialization
Wr
Wr
Rd
Rd
Wr
2
Wr
2
Rd
Rd
Wr
2
Wr
2
Rd
Rd
3
3
3
2. Write Penalty
3. Thrashing Row-Buffer
Served in parallel
Delayed

## Slide 7: Our Goal
Goal: Mitigate the detrimental effects of bank conflicts in a cost-effective manner
Naïve solution: Add more banks
  Very expensive
We propose a cost-effective solution

## Slide 8: Key Observation #1
A DRAM bank is divided into subarrays
Row
Row-Buffer
Row
Row
Row
32k rows
Logical Bank
A single row-buffer cannot drive all rows
Global Row-Buf
Physical Bank
Local Row-Buf
Local Row-Buf
Subarray1
Subarray64
Many local row-buffers, one at each subarray

## Slide 9: Key Observation #2
Each subarray is mostly independent…
  except occasionally sharing global structures
Global Row-Buf
Global Decoder
Bank
Local Row-Buf
Local Row-Buf
Subarray1
Subarray64
···

## Slide 10: Key Idea: Reduce Sharing of Globals
Global Row-Buf
Global Decoder
Bank
Local Row-Buf
Local Row-Buf
···
1. Parallel access to subarrays
2. Utilize multiple local row-buffers

## Slide 11: Overview of Our Mechanism
···
Req
Req
Global Row-Buf
Local Row-Buf
Req
Local Row-Buf
Req
1. Parallelize
2. Utilize multiple local row-buffers
Subarray64
Subarray1
To same bank...
but diff. subarrays

## Slide 12: Outline
Motivation & Key Idea
Background
Mechanism
Related Works
Results

## Slide 13: Organization of DRAM System
DRAM System
Bank
Rank
Bank
Rank
Channel
Bus
CPU

## Slide 14: Naïve Solutions to Bank Conflicts
More channels: expensive
More ranks: low performance
More banks: expensive
DRAM System
Channel
Channel
Channel
Channel
Bus
Bus
Bus
Bus
Many CPU pins
Channel
R
R
R
R
Low frequency
Channel
Rank
Bank
Significantly increases DRAM die area
Large load

## Slide 15: Logical Bank
data
Row
Row
Row
Row
wordlines
bitlines
Precharged
State
Activated State
0
0
0
ACTIVATE
PRECHARGE
addr
Decoder
VDD
?
Row-Buffer
RD/WR
0
Total latency: 50ns!

## Slide 16: Physical Bank
Row-Buffer
32k rows
very long bitlines: hard to drive
Global Row-Buf
Local Row-Buf
Local Row-Buf
Subarray1
···
Local bitlines: short
512 rows
Subarray64

## Slide 17: Hynix 4Gb DDR3 (23nm) Lim et al., ISSCC’12
Bank0
Bank1
Bank2
Bank3
Subarray
Subarray Decoder
Tile
Magnified
Bank5
Bank6
Bank7
Bank8

## Slide 18: Bank: Full Picture
Global Row-Buf
Local Row-Buf
Local Row-Buf
···
Local bitlines
Subarray64
Subarray1
Local bitlines
Global bitlines
Bank
Global Decoder
Subarray Decoder
Latch

## Slide 19: Outline
Motivation & Key Idea
Background
Mechanism
Related Works
Results

## Slide 20: Problem Statement
···
Req
Req
Global Row-Buf
Local Row-Buf
Local Row-Buf
Serialized!
To different subarrays

## Slide 21: Overview: MASA
MASA (Multitude of Activated Subarrays)
···
addr
VDD
addr
Global Decoder
VDD
Local Row-Buf
Local Row-Buf
ACTIVATED
Global Row-Buf
ACTIVATED
READ
READ
Challenges: Global Structures

## Slide 22: Challenges: Global Structures
  1. Global Address Latch
  2. Global Bitlines

## Slide 23: Challenge #1. Global Address Latch
Local row-buffer
Local row-buffer
Global row-buffer
···
addr
VDD
addr
Global Decoder
VDD
Latch
Latch
Latch
PRECHARGED
ACTIVATED
ACTIVATED

## Slide 24: Solution #1. Subarray Address Latch
Local row-buffer
Local row-buffer
Global row-buffer
···
VDD
Global Decoder
VDD
Latch
Latch
Latch
ACTIVATED
ACTIVATED

## Slide 25: Challenges: Global Structures
  1. Global Address Latch
    Problem: Only one raised wordline
    Solution: Subarray Address Latch
  2. Global Bitlines

## Slide 26: Challenge #2. Global Bitlines
Local row-buffer
Local row-buffer
Switch
Switch
READ
Global bitlines
Global row-buffer
Collision

## Slide 27: Solution #2. Designated-Bit Latch
Wire
Global bitlines
Global row-buffer
Local row-buffer
Local row-buffer
Switch
Switch
READ
READ
D
D
D
D

## Slide 28: Challenges: Global Structures
  1. Global Address Latch
    Problem: Only one raised wordline
    Solution: Subarray Address Latch
  2. Global Bitlines
    Problem: Collision during access
    Solution: Designated-Bit Latch

## Slide 29: MASA: Advantages
Baseline (Subarray-Oblivious)
MASA
time
Wr
2
Wr
2
Rd
Rd
3
3
3
1. Serialization
2. Write Penalty
3. Thrashing
time
Wr
Wr
Rd
Rd
Saved

## Slide 30: MASA: Overhead
DRAM Die Size: Only 0.15% increase
  Subarray Address Latches
  Designated-Bit Latches & Wire
DRAM Static Energy: Small increase
  0.56mW for each activated subarray
  But saves dynamic energy
Controller: Small additional storage
  Keep track of subarray status (< 256B)
  Keep track of new timing constraints

## Slide 31: Cheaper Mechanisms
D
D
Latches
1. Serialization
2. Wr-Penalty
3. Thrashing
MASA
SALP-2
SALP-1

## Slide 32: Outline
Motivation & Key Idea
Background
Mechanism
Related Works
Results

## Slide 33: Related Works
Randomized bank index [Rau ISCA’91, Zhang+ MICRO’00, …]
  Use XOR hashing to generate bank index
  Cannot parallelize bank conflicts
Rank-subsetting [Ware+ ICCD’06, Zheng+ MICRO’08, Ahn+ CAL’09, …]
  Partition rank and data-bus into multiple subsets
  Increases unloaded DRAM latency
Cached DRAM [Hidaka+ IEEE Micro’90, Hsu+ ISCA’93, …]
  Add SRAM cache inside of DRAM chip
  Increases DRAM die size (+38.8% for 64kB)
Hierarchical Bank [Yamauchi+ ARVLSI’97]
  Parallelize accesses to subarrays
  Adds complex logic to subarrays
  Does not utilize multiple local row-buffers

## Slide 34: Outline
Motivation & Key Idea
Background
Mechanism
Related Works
Results

## Slide 35: Methodology
DRAM Area/Power
  Micron DDR3 SDRAM System-Power Calculator
  DRAM Area/Power Model [Vogelsang, MICRO’10]
  CACTI-D [Thoziyoor+, ISCA’08]
Simulator
  CPU: Pin-based, in-house x86 simulator
  Memory: Validated cycle-accurate DDR3 DRAM simulator
Workloads
  32 Single-core benchmarks
    SPEC CPU2006, TPC, STREAM, random-access
    Representative 100 million instructions
  16 Multi-core workloads
    Random mix of single-thread benchmarks

## Slide 36: Configuration
System Configuration
  CPU: 5.3GHz, 128 ROB, 8 MSHR
  LLC: 512kB per-core slice
Memory Configuration
  DDR3-1066
  (default) 1 channel, 1 rank, 8 banks, 8 subarrays-per-bank
  (sensitivity) 1-8 chans, 1-8 ranks, 8-64 banks, 1-128 subarrays
Mapping & Row-Policy
  (default) Line-interleaved & Closed-row
  (sensitivity) Row-interleaved & Open-row
DRAM Controller Configuration
  64-/64-entry read/write queues per-channel
  FR-FCFS, batch scheduling for writes

## Slide 37: Single-Core: Instruction Throughput
Chart: IPC Improvement
| hmmer | leslie3d | zeusmp | Gems. | sphinx3 | scale | add | triad | gmean
MASA | 0.39452 | 0.4222 | 0.43858 | 0.4506 | 0.48602 | 0.48761 | 0.57109 | 0.57408 | 0.16722
"Ideal" | 0.49318 | 0.52653 | 0.4596 | 0.53601 | 0.51938 | 0.56315 | 0.79115 | 0.77408 | 0.19601
17%
20%
MASA achieves most of the benefit of having more banks (“Ideal”)

## Slide 38: Single-Core: Instruction Throughput
Chart: IPC Increase
| gmean
SALP-1 | 0.066253
SALP-2 | 0.13406
MASA | 0.16722
"Ideal" | 0.19601
SALP-1, SALP-2, MASA improve performance at low cost
20%
17%
13%
7%
DRAM Die Area | < 0.15% | 0.15% | 36.3%

## Slide 39: Single-Core: Sensitivity to Subarrays
Chart: Subarrays-per-bank
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
MASA | 0 | 0.082463 | 0.13688 | 0.16722 | 0.18437 | 0.19313 | 0.19761 | 0.19994
You do not need many subarrays for high performance

## Slide 40: Single-Core: Row-Interleaved, Open-Row
Chart: IPC Increase
| gmean
MASA | 0.1235
"Ideal" | 0.1471
15%
12%
MASA’s performance benefit is robust to mapping and page-policy

## Slide 41: Single-Core: Row-Interleaved, Open-Row
Chart: Normalized Dynamic Energy
| gmean
Baseline | 1
MASA | 0.81324
Chart: Row-Buffer Hit-Rate
| gmean
Baseline | 0.56896
MASA | 0.69801
MASA increases energy-efficiency
-19%
+13%

## Slide 42: Other Results/Discussion in Paper
Multi-core results
Sensitivity to number of channels & ranks
DRAM die area overhead of:
  Naively adding more banks
  Naively adding SRAM caches
Survey of alternative DRAM organizations
  Qualitative comparison

## Slide 43: Conclusion
Problem: Requests to same DRAM bank are serialized
Our Goal: Parallelize requests to same DRAM bank at a low cost
Observation: A bank consists of subarrays that occassionally share global structures
MASA: Reduces sharing to enable parallel access and to utilize multiple row-buffers
Result: Significantly higher performance and energy-efficiency at low cost (+0.15% area)

## Slide 44: A Case for Subarray-Level Parallelism (SALP) in DRAM
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, Onur Mutlu