## Slide 1: Introduction to Mobile Security
Dominic Chen
ddchen@cmu.edu
Carnegie Mellon University

## Slide 2: Goals
What’s different about mobile security?
  Non-homogeneous hardware architecture
  Device capabilities
  Attacker goals
  Software ecosystems

## Slide 3: Processor Architecture
Notes: http://www.bdti.com/InsideDSP/2012/06/21/Qualcomm

## Slide 4: Device Capabilities
Connectivity
  GPS
  Cellular Network (GSM/CDMA)
  WiFi
  NFC
Sensors
  Accelerometer
  Gyroscope
  Ambient Light
  Compass
  Barometer
  Fingerprint sensor
Battery-powered

## Slide 5: Malware Types
Chart: 
| Trojan (SMS) | RiskTool | Adware | Trojan | Monitor | Backdoor | Trojan (Financial) | Exploit | HackTool | Trojan (Downloader) | Others
Column1 | 57.08 | 21.52 | 7.37 | 3.44 | 2.72 | 2.54 | 1.98 | 1.62 | 0.59 | 0.5 | 0.64
Notes: http://media.kaspersky.com/pdf/Kaspersky-Lab-KSN-Report-mobile-cyberthreats-web.pdf

## Slide 6: Operating Systems
Notes: https://www.idc.com/prodserv/smartphone-os-market-share.jsp

## Slide 7: Software Ecosystem
Resource-limited devices
  Compute
  Power
Event-driven programming
  No main() method
  State transitions via callbacks
Well-defined interfaces
  Application lifecycle
  Access to user data
Centralized software distribution
  Can only download applications from a single source
  Vendor takes responsibility for filtering content
Notes: https://www.idc.com/prodserv/smartphone-os-market-share.jsp

## Slide 8: Overview
Architectural complexity
  New attack vectors
Mobile operating systems
  Operating system safety protections
  Software development and distribution model
Common problems with real-world software
  Cryptographic misuse
  Personal information leakage
Current research techniques

## Slide 9: Block Diagram (Nexus 5)
Notes: https://docs.google.com/file/d/0B7VNhP6LbXNmdl9wZG1OSTBnVUE/edit?pli=1

## Slide 10: Block Diagram (Baseband)
Notes: http://www.androidauthority.com/smartphones-have-a-second-os-317800/

## Slide 11: Baseband Processor
Separate processor or core that manages radio functionality (why?)
Typically runs a proprietary real-time operating system
  Apple iPhone: Nucleus RTOS, ThreadX
  Qualcomm: Advanced Mobile Subscriber Software (AMSS/REX OS)
    L4A Pistachio microkernel
Notes: Reasons: Timing-dependent, certification of entire radio software stack

## Slide 12: Boot Process
Notes: http://forum.xda-developers.com/showpost.php?p=30055671
http://forum.xda-developers.com/showpost.php?p=63862650&postcount=158

## Slide 13: ARM TrustZone
Notes: http://www.arm.com/products/processors/technologies/trustzone/tee-smc.php

## Slide 14: ARM TrustZone
Provides a separate hardware-enforced execution environment
  x86 protection rings (0, 3)
Applications
  Digital rights management
  Secure key storage
  Mobile payments
  Secure boot management (Q-Fuses)
  Kernel integrity monitoring

## Slide 15: ARM TrustZone
Qualcomm Secure Execution Environment (QSEE)
  Contains separate kernel with separate memory space
  Has privileged access to all hardware and the non-secure world
  Interfaces with the non-secure world via the privileged Secure Monitor Call (SMC) instruction
Notes: https://www.blackhat.com/docs/us-14/materials/us-14-Rosenberg-Reflections-On-Trusting-TrustZone-WP.pdf

## Slide 16: Case Studies
Baseband Attacks: Remote Exploitation of Memory Corruptions in Cellular Protocol Stacks, Ralf-Philpp Weinmann (WOOT 2012)
  Memory corruption in various baseband stacks led to injection/execution of arbitrary code
Reflections on Trusting TrustZone, Dan Rosenberg (BlackHat 2014)
  Integer overflow vulnerability led to arbitrary write of secure memory
TrustNone, Sean Beaupre (11/28/15)
  Signed comparison on unsigned user input led to arbitrary read/write of secure memory
Notes: https://www.usenix.org/system/files/conference/woot12/woot12-final24.pdf
https://www.blackhat.com/docs/us-14/materials/us-14-Rosenberg-Reflections-on-Trusting-TrustZone.pdf
http://theroot.ninja/disclosures/TRUSTNONE_1.0-11282015.pdf

## Slide 17: Overview
Architectural complexity
  New attack vectors
Mobile operating systems
  Operating system safety protections
  Software development and distribution model
Common problems with real-world software
  Cryptographic misuse
  Personal information leakage
Current research techniques

## Slide 18: Introduction: Android
Originally developed by startup in 2003
  Bought out by Google in 2005
  Publicly released in 2007
Mostly released under open source license
  Proprietary device-specific drivers distributed in binary form
  Access to Play Store and Google applications requires licensing agreement
    Fire OS, Baidu, Yandex.Store, etc

## Slide 19: Version History
Notes: https://commons.wikimedia.org/wiki/File:Android_historical_version_distribution_-_vector.svg

## Slide 20: Security Model
Utilizes a modified version of the Linux kernel
  Changes are slowly being merged back upstream
UNIX permission model for applications
  Mandatory sandbox as separate users (distinct UID)
Limited interface for inter-process communication
Applications are cryptographically signed and verified
Notes: https://source.android.com/security/overview/kernel-security.html

## Slide 21: Architecture: Android
Notes: http://androidteam.googlecode.com/files/Anatomy-Physiology-of-an-Android.pdf

## Slide 22: Safety Enhancements
Android 1.5+
  Stack overflow protection (-fstack-protector)
  Safe integer operations (-lsafe_iop)
  Double free protection
  Memory allocation integer overflow protection
Android 2.3+
  Format-string protections (-Wformat-security)
  Data execution protection (DEP)
  NULL pointer dereference protection (vm.mmap_min_addr)
Android 4.0+
  Address Space Layout Randomization (ASLR)
Notes: https://www.duosecurity.com/blog/exploit-mitigations-in-android-jelly-bean-4-1
https://source.android.com/security/enhancements/enhancements50.html
https://source.android.com/security/enhancements/enhancements60.html

## Slide 23: Safety Enhancements
Android 4.1+
  Position Independent Executables (PIE)
  Read-only relocations (-Wl,-z,relro –Wl,-z,now)
Android 5.0+
  Default full disk encryption
  Mandatory PIE
  SELinux
Android 6.0+
  Verified boot
  USB access control
  Monthly security patches
Notes: https://www.duosecurity.com/blog/exploit-mitigations-in-android-jelly-bean-4-1

## Slide 24: Permission Model
Capability-based access control model
Categorized into various functional groups
  Bluetooth
  Camera
  Location (fine/coarse-grained)
  Network/data connection
  SMS/MMS
  Telephony
User receives permission prompt at install-time
  All-or-nothing

## Slide 25: Permission Model
Notes: https://www.internetsafetyproject.org/wiki/android-permissions

## Slide 26: Permission Model
Notes: http://www.snoopwall.com/threat-reports-10-01-2014/

## Slide 27: Permission Model
Starting with Android 6.0 (Marshmallow), permissions are queried at run-time
  Allows users to deny individual permissions
  Was briefly available for Android 4.4.0 – 4.4.2
3rd party solutions
  Xposed Framework (requires root)

## Slide 28: Application Structure
Written in Java
  Interpreted by Dalvik bytecode virtual machine
    Uses just-in-time (JIT) techniques to compile native code
  Replaced with Android Runtime (ART) in 5.0+
    Introduces ahead-of-time (AOT) compilation instead of JIT
Can also call into native code
  Uses Java Native Interface (JNI) to interface with C/C++ libraries
Notes: http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=4768655

## Slide 29: Application Structure
Activity
  Portions of the application’s user interface
    Login window, registration interface, etc.
Service
  Performs background processing
    Download a file, play music, etc.
Broadcast Receiver
  Handlers for global messages
    Boot completed, power disconnected, etc.
Content Provider
  Manages access to structured data
    User calendar, contacts, etc.
Notes: http://ieeexplore.ieee.org/xpl/login.jsp?tp=&arnumber=4768655

## Slide 30: Case Studies
Stagefright, Zimperium (2015)
  Integer overflow vulnerabilities in system multimedia library leads to remote code execution
    Fixed in November monthly security patch
Master Key, Bluebox Security (2013)
  Structure of Android application packages allows manipulation of contents without invalidating digital signatures

## Slide 31: Introduction: iOS
Originally developed in 2005
  Publicly released in 2007
Based off of the Macintosh XNU kernel
  Supports memory-protection features
    ASLR, DEP, etc.
  UNIX-like

## Slide 32: Security Model
All applications must be signed by Apple
  Unless system is jailbroken to remove checks
Individual applications are encrypted and sandboxed from one another
Code integrity is verified during execution
  Makes injection of shellcode difficult

## Slide 33: Architecture: iOS
Notes: https://developer.apple.com/library/mac/documentation/MacOSX/Conceptual/OSX_Technology_Overview/MediaLayer/MediaLayer.html

## Slide 34: Application Structure
Written in Objective-C or Swift
  Compiled by Clang/LLVM into native code
  Adds automatic reference counting for garbage collection in Swift
    Transitioning to open source later this year
Uses Model-View-Controller (MVC) design paradigm
  Applications objects are model, view, or controller
  Abstracts data from logic and presentation
Notes: https://developer.apple.com/library/ios/documentation/General/Conceptual/DevPedia-CocoaCore/MVC.html

## Slide 35: Application Approvals
Applications are typically submitted by developers to App Store for inclusion
These undergo a review process for unwanted behavior or policy violations
  Objectionable content
  Game emulators
  Internal API’s
Techniques
  Static analysis
  Manual review

## Slide 36: Enterprise Provisioning
Enterprise developer certificates allow bypass of the App Store
  Designed for deployment of internal applications to employees
Historically, have also been used to bypass platform security
  Game emulators
  Jailbreaking
  Malware

## Slide 37: Case Studies
XcodeGhost, Alibaba (2015)
  Modified version of Xcode uploaded to a Chinese file sharing service inserted malicious code into binaries
Pangu8, Pangu Team (2015)
  Heap overflow in kernel battery gauge service for iOS 8 led to arbitrary writes of kernel memory
limera1n, George Hotz (2010)
  Heap overflow in bootloader USB protocol implementation led to arbitrary writes of memory

## Slide 38: Overview
Architectural complexity
  New attack vectors
Mobile operating systems
  Operating system safety protections
  Software development and distribution model
Common problems with real-world software
  Cryptographic misuse
  Personal information leakage
Current research techniques

## Slide 39: Common Problems
Developers are not experts in implementing or using cryptography
  Tendency to copy-paste “template” code
  Need to disable certain cryptographic features for ease of debugging
Developers tend to inadvertently or maliciously request extraneous permissions
  Can use user information for advertising or analytics

## Slide 40: Cryptographic Misuse
Usage of ECB mode for encryption
Usage of static IV’s in CBC mode
Usage of hardcoded symmetric encryption keys
Usage of low iterations for password-based encryption
Bad seeding of random-number generators

## Slide 41: Cryptographic Misuse
CryptoLint, Manuel Egele et al. (CCS 2013)
  Extract a control flow graph of an application
  Identify calls to sensitive cryptographic API’s
  Perform static backward slicing to evaluate security rules
Allows for automatic detection of cryptographic misuse

## Slide 42: Case Study

## Slide 43: Password Manager (2010)
private String encrypt(byte [] key, String clear) {
byte [] encrypted;
byte [] salt = new byte[2];
...
Random rnd = new Random();
//Cipher cipher = Cipher.getInstance("AES");
Cipher cipher =
Cipher.getInstance("AES/ECB/PKCS7Padding", "BC");
cipher.init(Cipher.ENCRYPT_MODE, skeySpec);
rnd.nextBytes(salt);
cipher.update(salt);
encrypted = cipher.doFinal(clear.getBytes());

## Slide 44: Password Manager (+6 days)
private String encrypt(byte [] key, String clear) {
byte [] encrypted;
byte [] salt = new byte[2];
...
Random rnd = new Random();
Cipher cipher =
Cipher.getInstance("AES/CBC/PKCS7Padding", "BC");
byte [] iv = {0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0};
IvParameterSpec ivSpec = new IvParameterSpec(iv);
cipher.init(Cipher.ENCRYPT_MODE, skeySpec, ivSpec);
rnd.nextBytes(salt);
cipher.update(salt);
encrypted = cipher.doFinal(clear.getBytes());

## Slide 45: Password Manager (+2yrs, 5mo)
private String encrypt(byte [] key, String clear) {
...
Random rnd = new Random();
Cipher cipher =
Cipher.getInstance("AES/CBC/PKCS7Padding", "BC");
byte [] iv = new byte[16];
rnd.nextBytes(iv);
IvParameterSpec ivSpec = new IvParameterSpec(iv);
cipher.init(Cipher.ENCRYPT_MODE,skeySpec,ivSpec);
encrypted = cipher.doFinal(clear.getBytes());
...

## Slide 46: Password Manager (key)
public static byte []
hmacFromPassword(String password) {
byte [] key = null;
...
Mac hmac = Mac.getInstance("HmacSHA256");
hmac.init (new SecretKeySpec
("notverysecretiv".getBytes("UTF-8"), "RAW"));
hmac.update(password.getBytes("UTF-8"));
key = hmac.doFinal();
...
return key;

## Slide 47: Developer Education

## Slide 49: Case Study
TaintDroid, William Enck et al. (OSDI 2010)
  Dataset of 30 randomly selected popular applications
  Flagged 105 TCP connections for containing tainted privacy-sensitive information
    Leakage of device IMEI
    Leakage of device location

## Slide 50: Overview
Architectural complexity
  New attack vectors
Mobile operating systems
  Operating system safety protections
  Software development and distribution model
Common problems with real-world software
  Cryptographic misuse
  Personal information leakage
Current research techniques

## Slide 51: Program Analysis
Taint Analysis
  Mechanism for identifying data flows in an application
Concepts:
  Basic Blocks
  Control Flow Graphs
  Call Graphs

## Slide 52: Basic Block
Sequence of instructions executed consecutively
  Only the first instruction can be reached from outside the block
  Only the last instruction may transition outside the block

## Slide 53: Basic Block
x = y + z
z = t + i
x = y + z
z = t + i
jmp 1
jmp 3
3 basic blocks

## Slide 54: Control Flow Graph
Each vertex is a basic block
There is an edge between two vertexes if there may be a transfer of control between the blocks
Typically limited to a single function or procedure (intraprocedural)

## Slide 55: Control Flow Graph
a = readline()
x = 0
if (a > 5) {
t = “gt”
x = 42
} else {
t = “lte”
x = 7
}
print(“input was ” +
t + “ 5”)
a = readline();
x = 0
if (a > 5)
print( … )
t = “lte”
x = 7
t = “gt”
x = 42

## Slide 56: Call Graph
Each node is a function
There is an edge between nodes if a function calls another

## Slide 57: Call Graph
void orange()
{
green();
red(); }
void red()
{
...
}
void green()
{
green();
orange();
}
orange
red
green

## Slide 58: Taint Analysis
Technique or identifying movement of data in an application
  Sources: Originations of privacy sensitive information, e.g. address book API
  Sinks: Destinations of network communication, e.g. socket API
Determine what flows occur between sources and sinks

## Slide 59: Challenges
Object-oriented languages encapsulate data as objects in memory
  Callbacks and local functions are used to transfer data
  Need to perform and propagate type recovery
Class hierarchy
  Determine relationships between parent and child classes
  Identify overridden and virtual functions
Handle dynamic object introspection
  e.g. Reflection

## Slide 60: Backward/Forward Slicing
Identify all instructions that may influence a given variable
  Program point
  Variable
Can be performed in both directions

## Slide 61: Backward/Forward Slicing
int main() {
int x, y, z;
x = 5 + 2 * 6;
y = getchar();
z = 8 + 10 % 3;
y = x + z * 5;
if (z > 9) {
x = 2 * z + 1;
} else {
x = 4 * z - 1;
}
y = 10 * y + 3;
return foo(x);
}
57

## Slide 62: Usage
Identify sources of data that is used in cryptographic API’s
  Constant values
  Uninitialized data
Identify sinks of data that originate from user data
  Address book
  Calendar
  IMEI

## Slide 63: Conclusion
Architectural complexity
  New attack vectors
Mobile operating systems
  Operating system safety protections
  Software development and distribution model
Common problems with real-world software
  Cryptographic misuse
  Personal information leakage
Current research techniques

## Slide 64
Questions?

## Slide 65: END