## Slide 1: Transactional Concurrency Control for Intermittent, Energy-Harvesting Computing Systems
Emily Ruppel and Brandon Lucia
June 26, 2019
PLDI 2019 -- Systems II

## Slide 2
Intermittent
Energy-Harvesting
Computing
Systems
Time
Energy
ML/AI beyond the edge
[Sonic & Tails, ASPLOS 2019]
Charging
Powered on
Power down
[Capybara, ASPLOS 2018]
Notes: -TODO: add power down
-On device side, need to mention that MCU has nonvolatile memory, mention briefly that we assume byte addressable

## Slide 3: Intermittent devices need concurrent interrupts
Atomic w.r.t power failures
Not intermittence safe
[Chain, OOPSLA 2016]
[Alpaca,
OOPSLA
2017]
Notes: Explain that intermittent systems fail approximately every 100ms

## Slide 4: Intermittent devices need concurrent interrupts
Event-atomic tasks
Multi-task transactions
Timely split-phase events
Notes: Need to slow down and be on point, there’s a lot going on here, and it’s important to explain it without losing people. Figure out what you want to say, and say it concisely.
Pay attention to two notions of atomicity

## Slide 5
Coati Motivation
Intermittent Programming Models & Interrupts
Problem #1: Interrupt Interrupted
Coati System Design
Coati Overview
Task & Event Interaction
Multi-Task Transactions
Coati Evaluation
Correctness
Programming Effort
Problem #2: False Flag
Runtime Overhead
Notes: TODO: figure out if there’s a good way to format the outline so the section we’re in is the only one with expanded bullet points

## Slide 6: Prior work supports one execution context
W = Z
Y++
assert(X==Y)
next_task send()
Z = X
X++
next_task incY()
task incX()
task incY()
Z = X
X++
W = Z
Y++
assert(X==Y)
[Alpaca,
OOPSLA 2017]
task
X = 0
Y = 0
event
Non-volatile
Write-after-read dependence
Idempotent re-execution
Notes: Note that all bold variables are stored in nonvolatile memory
-This talk focuses on statically declared tasks with statically defined control flow and arbitrary shared memory accesses made by tasks. To learn about reactive approaches, stick around for the next talk.
Computes long workloads despite frequent power failures, tasks are guaranteed to execute atomically, will repeatedly attempt to re-execute until we’re able to progress to the next task, able to decrease memory footprint by only versioning variables involved in WAR
Mention that this applies to checkpoints as well
Explain that X++ and Y++ are involved in a write-after-read dependence (not war)
Tasks: start from top, re-execute idempotently, communicate using global persistent variables
We put stuff into checkpoint to retain its value

## Slide 7: Interrupts violate correctness assumptions
W = Z
Y++
assert(X==Y)
next_task send()
Z = X
X++
next_task incY()
task incX()
task incY()
[Alpaca,
OOPSLA 2017]
Assumptions:
Tasks always start from the same point
Tasks re-execute idempotently
X = sense()
Notes: -Always assume that no matter where or how frequently a power failure happens, you’ll restart from the same program point (the top of the task)
-Assume re-execution is idempotent (rerunning the code will produce the same result)

## Slide 8: Power failures can happen during interrupts
X = 0
Y = 0
return
…
t1 = X + 1
…
t2 = Y + 1
assert(t1==t2)
next_task send()
task increment()
event clear()
X | Y
1 | 1
X | Y
0 | 1
Problem #1: Interrupt Interrupted
Notes: Can’t use an increment here because then we have a WAR, and then X and Y are under versioning from Alpaca -> Couch this as wanting to demonstrate a program that breaks even without WAR violations?
-don’t forget to mention that we changed the program –Mention that we assume this program is correctly synchronized
TODO: add code highlighting!!!!
Just say that the runtime system is not meant to handle interrupts, so on a power failure, it just regroups from the latest task as it usually would

## Slide 9: Conventional synchronization fails
…
T2 = Y + 1
assert(T1==T2)
flag = 0
next_task send()
if(flag)return
X = 0
Y = 0
return
…
flag = 1
T1 = X + 1
next_task incY()
task incX()
event clear()
task incY()
flag
0
flag
1
X | Y
1 | 1
X | Y
0 | 0
T1 | T2
0 | 0
T1 | T2
2 | 0
T1 | T2
2 | 2
T1 | T2
2 | 1
Problem #2: False Flag
Notes: What happens if we have to split into two tasks? We’ll show the synchronization code this time…
(The t2 values are based on t2 *not* being identified as a WAR. Technically it isn’t but I was under the impression Alpaca’s original implementation would conservatively version T2
TODO: add code highlighting!!!!
Explain the programmer’s intent was to have X+1 and Y+1 execute without an intervening interrupt
Emphasize that this only comes about because we mixed intermittent execution with interrupts
Remind people that this doesn’t go into the checkpoint b/c not WAR

## Slide 10
Coati Motivation
Intermittent Programming Models & Interrupts
Problem #1: Interrupt Interrupted
Coati System Design
Coati Overview
Task & Event Interaction
Multi-Task Transactions
Coati Evaluation
Correctness
Programming Effort
Problem #2: False Flag
Runtime Overhead
Notes: TODO: figure out if there’s a good way to format the outline so the section we’re in is the only one with expanded bullet points

## Slide 11: Coati produces correct code with interrupts for intermittent systems
App code
Programmer
Coati Application
Deployed App
Coati Binary
Coati Executable
Linker
App Binary
Coati Runtime
Intermittent Device

## Slide 12: Coati serializes interrupts after scheduled tasks
X = sense()
event_return()
transaction
Atomic w.r.t power failures
& events
Atomic w.r.t events
not power failures
…
Y++
assert(X == Y)
next_task send()
…
X++
next_task incY()
task incY()
task incX()
event sensor()
Notes: We want events to serialize after
Transactions provide simple, multi-task atomic regions to get rid of the flag nonsense
Coati provides the appearance of sequential semantics. The event serializes after the entire transaction completes

## Slide 13: Split-phase events provide timely reaction
X’ = senseX()
Y’ = senseY()
top_return(sensor)
top sensor()
AvgX = movingAvg(X’)
AvgY = movingAvg(Y’)
bottom sensor()
X = senseX()
Y = senseY()
AvgX = movingAvg(X)
AvgY = movingAvg(Y)
evt_return()
event sensor()
Schedules bottom half
Private Variable

## Slide 14: Split-phase serialization orders tasks & events
X’ = senseX()
Y’ = senseY()
evt_return(sensor)
…
X++
…
Y++
assert(X==Y)
next_task send()
task increment()
top sensor()
AvgX = movingAvg(X’)
AvgY = movingAvg(Y’)
bottom sensor()
task send()
Notes: Fix audio, make this smoother. Add in slide that explains split phase events
Be declarative with what’s happening

## Slide 15: Coati serializes multiple interrupts in FIFO order
…
evt_return(sensor)
…
X++
next_task send()
task incX()
top sensor()
…
bottom sensor()
…
Y++
assert(X==Y)
tx_next send()
task incY()
…
evt_return(sensor)
top sensor()
…
bottom sensor()
task send()
…
Notes: Emphasize that transactions fix the false flag problem
Consecutive events serialize in FIFO order. Later events can see the effects of previous events.
Be declarative with what’s happening
Jump to final animation  don’t worry about explaining that

## Slide 16
Coati Motivation
Intermittent Programming Models & Interrupts
Problem #1: Interrupt Interrupted
Coati System Design
Coati Overview
Task & Event Interaction
Multi-Task Transactions
Coati Evaluation
Correctness
Programming Effort
Problem #2: False Flag
Runtime Overhead
Notes: TODO: figure out if there’s a good way to format the outline so the section we’re in is the only one with expanded bullet points

## Slide 17
  Correctness
  Programming Effort
  Runtime Overhead
Coati Evaluation
Notes: Declarative, we show x, y, z

## Slide 18: We evaluated Coati on real hardware
Systems
Coati
Alpaca
Atomic
Hand-Optimized
Apps | 
Bitcount | BC
Activity Recognition | AR
RSA Encryption | RSA
Cold-Chain Equipment Monitor | CEM
Cuckoo Filter | CF
Blowfish Encryption | BF
Notes: Less time on platform, good job explaining how interrupts are worked into the benchmarks (rather than using canned data we rely on interrupts to indicate that new data are available) Explain how each kernel works, e.g. RSA pulls data into a buffer and encrypts. Clearly state that we’ll explain the systems as we go

## Slide 19: Coati ensures correct execution with interrupts
 | Coati | Alpaca
BC |  | 
AR |  | 
RSA |  | 
CEM |  | 
CF |  | 
BF |  | 
Synchronization was carefully added to the Alpaca code
Both systems used the same task decomposition
Data in Alpaca still become inconsistent
Notes: Explain what I mean by correctness, explain how we instrumented the code

## Slide 20: Coati transactions simplify concurrent code
Chart: Norm, L.o.C for Sync
| BC | AR | RSA | CEM | CF | BF
Coati | 1 | 1 | 1 | 1 | 1 | 1
Hand-Op | 4.3333 | 10 | 5 | 1.1429 | 8 | 2.4
 | 0 | 0 | 0 | 0 | 0 | 0
Lines of synchronization code reduced by 67% on average
Chart: Transitions for Sync
| BC | AR | RSA | CEM | CF | BF
Coati | 7 | 3 | 2 | 1 | 2 | 0
Hand-Op | 14 | 9 | 0 | 1 | 3 | 0
On average, fewer, simpler transitions are required
Notes: Explain what handop is
Explain that LoC is questionable proxy, paper digs into where those lines went. Coati makes it easier
An interesting stat to dig into- Hand-Op requires the programmer to add additional, very carefully placed transitions to get synchronization correct, in Coati you just instrument task transitions
TODO: figure out why powerpoint is terrible and I can’t change the font size in the graph, add red line at 1 for norm
Emphasize that handop requires ad-hoc, per program synchronization. It’s difficult because the programmer has to consider when a power failure could occur, like writing low level concurrency code.
Axes on talk

## Slide 21: Coati’s overhead is similar to other strategies
Chart: Runtime on Harvested Energy
| BC | AR | RSA | CEM | CF | BF
Atomic | 96.0315 | 190.4008 | 130.0488 | 120.1356 | 85.4341 | 123.0005
Hand-Op | 86.098 | 183.5305 | 97.9591 | 91.0935 | 81.3933 | 131.0394
Coati | 82.5765 | 189.9294 | 98.969 | 103.8828 | 83.2043 | 125.283
without their drawbacks
Notes: Figure out why powerpoint has decided we need a coati in the wrong spot…
Cleanup the description of the downside of atomic

## Slide 22: Coati provides simple, correct semantics for concurrency control in an intermittent execution
For more:
Read the paper
Experiment with our code
Stick around!
github.com/CMUAbstract/coati_pldi19.git
Notes: Give a shout out to Kiwan

## Slide 23: Transactional Concurrency Control for Intermittent, Energy-Harvesting Computing Systems
Emily Ruppel and Brandon Lucia
June 26, 2019
PLDI 2019 -- Systems II