## Slide 1: Wireless Network Security
Vyas Sekar

## Slide 2: This lecture’s agenda
Objective
  Understand in more details unique challenges of wireless networks
    WLAN and GSM
  Understand design flaws in supposedly secure protocol
  Gain exposure to real threat
    Know why you should never use WEP in an environment where security is important

## Slide 3: Wireless communications
Easy to eavesdrop on or tamper with!

## Slide 4: Need for over-the-air crypto
Easy to intercept traffic with regular equipment
Can be done from afar
  RF leakage
    May span several blocks
No privacy, confidentiality, integrity guaranteed at all

## Slide 5: WEP
Shared key (statically configured master)
Uses a stream cipher

## Slide 6: WEP encryption
WEP uses the RC4 stream cipher to encrypt a TCP/IP packet (P) by xor-ing it with keystream (RC4(K, IV))
IV
CRC-32
…
Payload
Key ID byte
RC4 encrypted
P  RC4(K, IV)

## Slide 7: A property of RC4
Keystream leaks, under known-plaintext attack
  Suppose we intercept a ciphertext C, and suppose we can guess the corresponding plaintext P
  Let Z = RC4(K, IV) be the RC4 keystream
  Since C = P  Z, we can derive the RC4 keystream Z by P  C = P  (P  Z) = Z
This is not a problem ... unless keystream is reused!

## Slide 8: A risk of keystream reuse
If IV’s repeat, confidentiality is at risk
  If we send two ciphertexts (C, C’) using the same IV, then the xor of plaintexts leaks (P  P’ = C  C’), which might reveal both plaintexts
  If there is redundancy, if we can guess one plaintext, etc…
IV, P  RC4(K, IV)
IV, P’  RC4(K, IV)

## Slide 9: IV selection
IV reuse implies keystream reuse
  Since keystream function only of IV and fixed master key
IV changes after every packet, but only 224 = 16,777,216 possible values (from the standard)
  Will definitely repeat after a while
    1500 byte-packets, 5 Mbps: repeats after half a day
    This is a best-case - random selection of IV after each packet yields collisions after 5,000 packets
Initial IV value (after boot) often picked to be zero
  Rebooting may cause IV reuse
Confidentiality is not guaranteed

## Slide 10: Spoofed packets I: tampering
CRC is linear
  I.e. CRC(X  Y) = CRC(X)  CRC(Y)
Stream cipher has following property
  RC4(k, IV, X  Y) = RC4(k,IV)  X  Y
So:
  RC4(k, IV, CRC(XY)) = RC4(k,IV)  CRC(X) CRC(Y)
IV
CRC-32
…
Payload
Key ID byte
RC4 encrypted
P  RC4(K, IV)
All you need to do is to compute the checksum of the modification , CRC(D) and XOR it to the message!

## Slide 11: Spoofed packets II: injection
CRC is unkeyed
If attacker can intercept one value of RC4(k,IV) (through a plaintext/ciphertext pair, for instance), it is possible to forge a packet
  C’ = < M’, CRC(M’) >  RC4(k, IV)
It implies reuse of IV, but this is permitted by the protocol
IV
CRC-32
…
Payload
Key ID byte
RC4 encrypted
P  RC4(K, IV)
Arbitrary injection of packets is possible

## Slide 12: Defeating WEP authentication
Access point sends plaintext challenge
End-host replies with RC4-encrypted challenge
Assumes that possession of the key means proof of identity
Attack
  Record first challenge-response, obtain keystream
  Reuse keystream next time
You don’t need the key to authenticate yourself

## Slide 13: Using the access point as an oracle
Arbitrary injection allows arbitrary decryption
  Sniff encrypted packet
  Modify destination address to an address on the Internet
  Replay packet
  AP will decrypt it for you!
A little tricky: requires modification of the IP checksum
  Difficult without the key
  But can always compensate for checksum changes by modifying other header fields

## Slide 14: Reaction attacks
Inject packets in network
See reaction of systems
For instance, slightly modify TCP packet
See if acknowledgment appears
  If it does, checksum still valid
  Meaning that you managed to “guess” correctly part of the packet
Details in paper

## Slide 15: Cryptographic problems
Fluhrer et al. came up with a recent attack on RC4
  http://en.wikipedia.org/wiki/Fluhrer,_Mantin_and_Shamir_attack
Designer’s worst fear: new flaw in encryption algorithm
Attack:
  Monitor encrypted traffic
  Look for special IV values that reveal information about key state
  Recover key after several million packets

## Slide 16: WEP conclusions
Security architecture does not meet its goals
  No confidentiality
    Plaintext may be recovered because of IV reuse
  No integrity
    Arbitrary modification or injection of messages is possible
And… RC4 actually turns out to not be as secure as previously thought
  Software is available so you don’t need any expertise
  Now you understand why we don’t use WEP here
… but many people still do!

## Slide 17: Global System for Mobile Communications (GSM)
One of the first digital mobile systems after analog era
Over 100 million subscribers
Primary cellular network in Western Europe/Africa/(most of) Asia
  US: AT&T and T-Mobile
Limited use in Japan or South Korea
  Except for “roaming”

## Slide 18: GSM overview
Cellular network
  Mobile devices connect to it by searching for cells in the immediate vicinity of the device
(Mostly) Four different frequency ranges
  900 MHz, 1800 MHz most popular
  US, Canada use 850 MHz and 1900 MHz bands
    900 and 1800 MHz frequency bands were already allocated
  (Scandinavia also uses 400-450 MHz band)
  “Quad”-band phones operate in all bands …
Codecs compress 3.1kHz audio into between 6 and 13kbps

## Slide 19: GSM security objectives
Avoid pitfalls of old analog cell phones
Resilient to cloning (and therefore to impersonation)
  Should be impossible to call using someone else’s account
Resilient to eavesdropping
  Analog calls were not encrypted at all
  Should be impossible to eavesdrop using antenna or similar receiving equipment
Details were not public, but were reverse-engineered
  Unclear if it was to add more security or due to other concerns?

## Slide 20: GSM network structure
[from: Wikipedia]

## Slide 21: GSM network structure
[from: Wikipedia]
Base transceiver station
Base station controller
Home location register + Authentication center
Mobile services switching center + Visitor location register
Receivers: identified by SIM card

## Slide 22: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
Base station

## Slide 23: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
Base station

## Slide 24: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
Base station
2. request triples

## Slide 25: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
3. (RAND, SRES, Kc) x 5
Base station
2. request triples
RAND = random number
SRES = A3Ki(RAND)
Kc = A8Ki(RAND)

## Slide 26: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
3. (RAND, SRES, Kc) x 5
4.RAND
Base station
2. request triples
RAND = random number
SRES = A3Ki(RAND)
Kc = A8Ki(RAND)
4. Kc

## Slide 27: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
3. (RAND, SRES, Kc) x 5
4.RAND
5. SRES
Base station
2. request triples
RAND = random number
SRES = A3Ki(RAND)
Kc = A8Ki(RAND)
4. Kc

## Slide 28: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
3. (RAND, SRES, Kc) x 5
4.RAND
5. SRES
Base station
2. request triples
RAND = random number
SRES = A3Ki(RAND)
Kc = A8Ki(RAND)
6. SRES ok!
4. Kc

## Slide 29: Security model
Mobile
station
HLR/AuC
MSC/VLR
Ki
Ki
1. first time
sign on
3. (RAND, SRES, Kc) x 5
4.RAND
5. SRES
Base station
2. request triples
RAND = random number
SRES = A3Ki(RAND)
Kc = A8Ki(RAND)
6. SRES ok!
4. Kc
7. A5Kc(talk)

## Slide 30: Authentication and key generation
A3
Ki (128 bit), RAND (128 bit)
Ki (128 bit), RAND (128 bit)
A8
Kc (64 bit)
SRES (32 bit)

## Slide 31: Authentication and key generation
In practice, however… A3 = A8 = COMP128
COMP128
Ki (128 bit), RAND (128 bit)
SRES
K’c
128 bits
32 bits
54 bits

## Slide 32: Authentication and key generation
In practice, however… A3 = A8 = COMP128
Done in ALL
implementations!
  including non COMP128
COMP128
Ki (128 bit), RAND (128 bit)
SRES
K’c
128 bits
32 bits
54 bits
K’c
0000000000
64 bits
Kc:

## Slide 33: Over-the-air encryption

## Slide 34: Over-the-air encryption
A5
Kc (64 bit),
Frame number (22 bit)
114-bit keystream
+
Plaintext
(frame)
Ciphertext
A5
Kc (64 bit),
Frame number (22 bit)
114-bit keystream
+
Plaintext

## Slide 35: Over-the-air encryption
A5
Kc (64 bit),
Frame number (22 bit)
114-bit keystream
+
Plaintext
(frame)
Ciphertext
A5
Kc (64 bit),
Frame number (22 bit)
114-bit keystream
+
Plaintext
!!

## Slide 36: A5/x algorithm family
A5/0: no encryption
A5/1: LSFR (Linear-shift-feedback register)-based, supposedly 64-bit strong
  But already limited to 54-bit b/c of Kc computation
  Completely broken in 2010 (Nohl et al.)
A5/2: weaker
  Used for export to “some” countries
  Can be broken in real time using low end equipment (Goldberg & Wagner)

## Slide 37: Attacks on GSM
Crypto attacks on A5 algorithms
Accessing the signaling network
SIM cloning
Cracking COMP128?

## Slide 38: Crypto attacks
Brute force: 54-bit, doable but expensive
  The same Kc may be in use for days…
Known plaintext attack (1997): O(245)
  Determine the initial state of the LSFR through known keystream sequence
  Only need 64 known bits!
  Can be optimized to O(240)
More recent attacks (2000-)
  Can break A5/1 in minutes with only 2 or 3 minutes of plaintext conversation
  Can break A5/1 through a ciphertext-only attack
    Rainbow-tables (2008), pre-computation attacks (2010)
  Active attack: phone can be made to use A5/2 for a few minutes
    The same Kc is used and can be easily recovered then!!

## Slide 39: Accessing the signaling network

## Slide 40: Accessing the signaling network
encrypted
unencrypted

## Slide 41: Accessing the signaling network
encrypted
unencrypted
Points of attack

## Slide 42: Accessing the signaling network
encrypted
unencrypted
Points of attack

## Slide 43: BTS to BSC
Simple cable
  Easy to wiretap if not properly secured physically
  Can go undetected for a long time!
Satellite link
Microwave link
  With the right type of equipment, easy to eavesdrop on if no crypto

## Slide 44: SIM cloning
Everything hinges on Ki
If you get my Ki, you can impersonate me
  Placing a call while I am calling results in the account being cancelled…
  … but still possible to eavesdrop at will
Problem: COMP128 broken
  With the “right” RAND values given, one can recover Ki from SRES!
  150,000 challenges + differential cryptanalysis
  Easy to do if SIM card is physically available for a couple of hours

## Slide 45: SIM cloning over the air
Same attack can be launched remotely
  Base Tower Station does not authenticate itself
  So, if you can overpower the BTS, you can pose as a legitimate tower and start issuing challenges
  Not so hard to do when your phone gets bad signal or no signal
    Subway, buildings (e.g., the CIC in Pittsburgh a couple of years ago), …

## Slide 46: GSM conclusions
Security architecture does not meet its goals
  Too many possible weak links in the network
  Questionable cryptographic strength
  Single point of failure (KI)
  No mutual authentication
All of this found through reverse-engineering
  Maybe the design process should have been more open…

## Slide 47: Take away slide
Wireless networking is convenient, but physical channel is completely insecure
Definitely need security at the link layer
Not easy to do!
WEP and GSM are both examples of how badly things can be broken
  Meet none of their security objectives
  Questionable use of crypto, cryptographic flaws, architectural flaws, multiple violations of secure design principles, …

## Slide 48: Poster guidelines
We will send poster templates/examples
Make it visual/interesting, don’t dump text!
Some useful advice on the web
  http://www.nuigalway.ie/remedi/poster/media/Posters_Good_and_bad.pdf
  http://colinpurrington.com/2012/example-of-bad-scientific-poster/
  https://www.youtube.com/watch?v=PLuMRqcZhrI
  https://www.youtube.com/watch?v=agtgnJP3KoQ
Start early -- Happy to give you feedback!

## Slide 49: Prizes!
Top two projects/posters
  Most likely: Gift cards from the bookstore
  Bragging rights 
Judging: We will have votes from you/visitors/course staff
Most important: Have fun 