## Slide 1: Network intrusion detection
Vyas Sekar

## Slide 2: Firewalls
Block/filter/modify traffic at network-level
  Limit access to the network
  Installed at perimeter of the network
Allows traffic specified in the policy
Drops everything else
Internet
Internal Network
Firewall

## Slide 3: Typical Firewall Configuration
Internal hosts can access DMZ and Internet
External hosts can access DMZ only, not Intranet
DMZ hosts can access Internet only
Advantages?
  If a service gets compromised in DMZ it cannot affect internal hosts
Internet
Intranet
DMZ
X
X

## Slide 4: Intrusion Detection Systems
Firewalls allow traffic only to legitimate hosts and services
Traffic to the legitimate hosts/services can have attacks
Solution?
  Intrusion Detection Systems
  Monitor data and behavior
  Report when identify attacks

## Slide 5: This lecture’s agenda
Outline
  Overview of IDS systems
  Bro overview
  NIDS evasion
  Normalization
Objective
  Get a detailed understanding of modern network intrusion detection systems
    Limitations
    Trade-offs
    Usefulness

## Slide 6: IDS justification
Comments on IDS
  “IDS easy to circumvent”
  “Installing IDS is useless”
  “Impossible to design bulletproof IDS”
Responses
  IDS is one component of a security system: Prevention, Detection & Recovery, Redundancy
  Increases difficulty of successful attack: “Raising the bar”
  If system defends against 95% of attackers, we can concentrate on the remaining 5%

## Slide 7: Firewall vs. NIDS
Firewall
  Active filtering
  Fail-close
Network IDS
  Passive monitoring
  Fail-open
Advantages and disadvantages?
Internet
FW
Internet
NIDS

## Slide 8: Evolution of the IDS
Notion that audit/log data might help to discover abuse/misuse dates to early 1970s
Framework for analysis established by Jim Anderson in 1980 in “Computer Security Threat Monitoring and Surveillance” http://seclab.cs.ucdavis.edu/projects/history/CD/ande80.pdf
Computers can generate lots of log/audit data
Early analysis techniques were based on analysis of this audit data, and used a mix of statistical and AI based techniques

## Slide 9: Evolution of the IDS
By the late 1980s, networked computers were increasingly common and many intrusions involved external access via a network
The Network Security Monitor developed at the University of California Davis was the first IDS to work directly with network data as opposed to log data
  Essentially a packet sniffer feeding data to an analysis engine

## Slide 10: Evolution of the IDS
Today, the vast majority of IDS systems are based on the analysis of network traffic.
There are numerous commercial offerings as well as a number of research systems and systems offered by the open source community.
Increasingly, the administration of IDS systems is integrated into system and network management frameworks.

## Slide 11: Types of IDS
Network-based
Signature-based
Anomaly-based
Host-based

## Slide 12: Signature-based IDS
Characteristics
  Uses known pattern
  matching to signify
  attack
  Can identify intrusions from packet header/data
  May use Boolean operators in rule set
    ‘this_string’
    ‘this_variable’ AND ‘that_number’
    ‘this_string’ AND ‘that_variable’ NOT ‘that_tcp_flag’

## Slide 13: Signature-based IDS
Advantages
  Widely available
  Fairly fast
  Not overly complex
  Easy to implement
  Easy to update
Example?
Notes:   Widely available
  Fairly fast
  Not overly complex
  Easy to implement
  Easy to update

## Slide 14: Signature-based IDS
Disadvantages
  Cannot detect attacks for which it has no signature
  May be resource intensive
  Must be updated for each new attack and attack variant
  Lag time from new exploit to update can be dangerous
  ‘New’ attack variant can be created by changing a single string

## Slide 15: Anomaly-based IDS
Characteristics
  Uses statistical model or machine learning engine to characterize normal usage behaviors
  Recognizes departures from normal as potential intrusions

## Slide 16: Anomaly-based IDS
Advantages
  Can detect attempts to exploit new and unforeseen vulnerabilities
  Can recognize unusual traffic based on a number of characteristics:
    Payload
    Source address
    Time
  Can recognize authorized usage that falls outside the normal pattern

## Slide 17: Anomaly-based IDS
Disadvantages
  Generally slower, more resource intensive compared to signature-based IDS
  Greater complexity, difficult to configure
  Higher percentages of false alerts
    Link between abnormal and intrusive may be weak

## Slide 18: Anomaly-based IDS
Typical deployment environments
  Currently few typical deployments
    Anomaly-based IDS considered immature, too error-prone for widespread use
    Exceptions in DDoS area
Example?

## Slide 19: Network-based IDS
Characteristics
  Network monitor
    Passively captures traffic and inspects
    it
  Can also function in a client-server model
    Sensors are located on multiple machines across the network
    All sensors feed data to console
    Console machine handles logging and alerting

## Slide 20: Network-based IDS
Advantages
  Positioned properly, can test effectiveness of firewalls, router access lists, etc.
  Can monitor multiple machines from one physical and logical location
  Console can generate an alert if a monitored machine/network has ceased to send information
  Operator can see patterns in traffic
    Amount
    Type

## Slide 21: Network-based IDS
Disadvantages
  Since it is capturing all network packets, can produce large log/alert files
    Can be difficult to cull through vast amount of information
  Console machine generally must be quite powerful, similar to a workgroup server
  If console machine goes down then multiple machines may be left unmonitored
  Communication from sensors to console may increase overall network traffic levels
Example

## Slide 22: Host-based IDS
Characteristics
  Runs on single host
  Can analyze audit-trails, logs, integrity of files and directories, etc.
    Tripwire, Fcheck
    RealSecure® Server Sensor
    Research systems such as Emerald
  May report to central administrative console

## Slide 23: Host-based IDS
Advantages
  Relatively easy to deploy and to manage
    Only one machine is involved
    May require only one administrator
    Creates single source of log and alert information
  Generally not resource intensive - in most cases
    Often will not require CPU, memory, etc. beyond what is needed for OS and applications

## Slide 24: Host-based IDS
Disadvantages
  Works well for single machine; extremely labor-intensive to monitor multiple machines each running a host-based IDS
  If the host is compromised, the IDS may cease to function and thus no more alerts will be generated

## Slide 25: Host-based IDS
Typical deployment environments
  Single mission-critical machine that can be monitored from the console
  User’s desktop machine, e.g. a DSL or cable user’s system

## Slide 26: Bro: Detecting intruders in real-time
Bro is a standalone NIDS developed by Vern Paxson
Designed to keep LBL an open environment (to resist the need to install a firewall)
Goals
  High-speed monitoring, no packet drops
  Real-time notification
  Separate mechanism from policy
  Extensibility
  Simple to use, guard against mistakes
  Tolerate attacks on NIDS
More powerful than Snort, but less popular. Why?
Misuse detection (signature-based) or anomaly detection (specification-based or statistical-based)?
Notes: Bro was so good that red team was unable to attack LBL. They tried to do network scanning, and they would be turned off after a few scanning packets. The NSA then helped them trying to break in, they were exposed because all the attacks happened 8am-5pm EST.

## Slide 27: Bro rules vs. Snort signatures
HTTP server attack
  Snort signature: simple pattern matching on MS ISS attack
  Bro rule: additional check to see if, e.g., host is running Apache  ignore alarm
Error code checking
  Snort signature: no checking of reply
  Bro rule: Looks at return code for HTTP/FTP/SMTP,
    signature match + error code = no alert
Multi-stage attacks
  Easy in Bro to express “signature A but only if followed by signature B” or “A unless followed by B”
  Easy to express “generate alarms if given host triggers N or more signatures” or “triggers against N or more local hosts”
Greatly reduces number of false positives!
(from Brian Tierney)

## Slide 28: Bro system architecture
Network
libpcap
Event Engine
Policy Script Interpreter
Packet stream
Filtered packet stream
Event stream
Alerts/notifications
Policy script
Event control
tcpdump filters

## Slide 29: libpcap Layer
Only passes relevant packets to Event Engine
Uses BSD Packet Filter (BPF) to efficiently filter packets
Filter rules
  tcp port finger or tcp port ftp or tcp port telnet or port 111 or tcp[13] & 7 != 0
What attacks will not be seen?
Notes: port 111 is portmapper
tcp[13] & 7 captures SYN, FIN, or RST packets
attacks not seen: tcp hijacking, tcp poisoning

## Slide 30: Event engine
State for each connection, based on <SrcIP, SrcPort, DstIP, DstPort>
  If state not present, allocate fresh state
TCP processing
  Update state based on SYN/FIN/RST flags
  Process acknowledgment
  SYN generates a timer event, if nothing happens after 5 min, generate connection_attempt event
UDP processing
  Initial packets generate udp_request and udp_reply events

## Slide 31: Policy script interpreter
Clear separation of event generation and response to achieve clear separation between mechanism and policy
  Advantage: extensibility (adding a new protocol analyzer and new event handler usually separate from other components)
Policy script interpreter executes event handlers

## Slide 32: Attacks on Bro monitor
Assumption: policy script is secret
  Good assumption?
Overload attack
  Exhaust computation resources
  Defense: lower the load (e.g., stop capturing HTTP traffic), effective if attacker does not know how Bro lowers load
Crash attack
  Find packet sequence that crashes monitor
  Exhaust memory, disk resources
  Defense: OS-level watchdog timer with subsequent packet capturing (sacrificing real-time detection)
Subterfuge attack
  Mislead monitor
Notes: Assumption that script is secret is not reasonable, as most sites will only make small changes to the default file. Violates Kerkhoff’s principle.

## Slide 33: Application-specific processing
Finger
  Finger policy looks for buffer overflow attacks against fingerd and detect finger for sensitive user IDs
Detect malicious activities for other protocols
  FTP
  Portmapper
  Telnet
What malicious activities can we find?

## Slide 34: Algorithmic complexity attacks
DoS attacks not only serious for denying service, but can be more severe by using it as a component of an attack
DoS attack on IDS enables other attacks to remain undetected
“Denial of Service via Algorithmic Complexity Attacks” by Crosby and Wallach

## Slide 35: Complexity attack on hash table
On average, a hash table has O(n) overhead to insert n elements
In the worst case, a hash table may have O(n2) overhead to insert n elements!
Attack against Perl hash table:

## Slide 36: Complexity attack against Bro
Bro uses simple 4-byte xor to “hash” values for hash table
Example: Bro port scanning detector keeps a hash table of source IP addresses
Using source IP spoofing, can exploit this structure to perform DoS attack!

## Slide 37: Bro attack results

## Slide 38: Where is this work now?

## Slide 39: NIDS: evasion & normalization
Problems
  Complete fragment reassembly necessary to detect certain attacks
  NIDS only has partial knowledge of what traffic the host sees (e.g., TTL expires, MTU)
  Ambiguities in TCP/IP (e.g., Overlapping IP & TCP fragments)
    Different OS implement standard differently
Approach: traffic normalization

## Slide 40: Small TTL attack
same TCP seq #, “I” has short TTL
Internet
NIDS
Host
End-host sees:
Attacker’s data stream
A
T
T
I
A
C
K
A
T
T
A
C
K
A
NIDS sees:
T
T
I
A
C
K

## Slide 41: Fragmentation overlap attack
Internet
End-host sees:
NIDS sees:
Attacker’s data stream
NIDS
Host
A
T
T
A
I
C
K
same TCP seq #
or same IP frag offset
A
T
T
A
I
C
K
A
T
T
A
I
C
K

## Slide 42: Approach: traffic normalizer
Introduce “bump in the wire”: traffic normalizer to evade protocol ambiguities
Other approaches
  Host-based IDS
  Detailed Intranet map
  Bifurcating analysis
Internet
NIDS
Host
Normalizer

## Slide 43: Normalization tradeoffs
Normalization vs. protection
  Off-load firewall/NIDS functionality
End-to-end semantics
  Drop overlapping IP/TCP fragments
  Increase TTL in packets with low TTL
    What applications does this break?
Keeping state
  “Fail closed” possible, given sufficient state
  DoS through state exhaustion is a challenge
Inbound vs. outbound traffic
  Normalize outbound traffic to ensure end-to-end semantics & to prevent unintended internal information from escaping
Notes: Increase TTL breaks traceroute & TTL based filtering

## Slide 44: Real-world considerations
Cold start
  Normalizer will reboot periodically
  Need to carefully design normalizer not to disturb established connections
Attacks against normalizer
  State exhaustion attacks
    Note: dropping a packet is ok, IP is unreliable
    Fragment reassembly by normalizer, can we do better? Security after forced reboot?
    SYN flooding, ACK flooding (allocate state to deal with cold start), unacknowledged data flooding
  CPU overload attacks
Notes: Purpose of fragment reassembly is to ensure that no fragment data overlaps, therefore, we only need to construct a duplicate (yet different!) data detector.
Occasionally dropping a packet is ok, IP is unreliable.

## Slide 45: Identifying normalizations
Consider each header field
  Identify range of values, semantics, and ways attacker can use it
  Find ways to normalize it
  Analyze impact on protocols
Approach: identify fields that may cause packet to be dropped/misinterpreted by router or endhost
Notes: 1. Identify packets that may be dropped/misinterpreted by router or endhost

## Slide 46: Stealth portscan
IP id field used for stealth port scanning
Permute IP id deterministically prevents internal hosts from being misused as patsies
Reliable RST protects internal hosts from being victims

## Slide 47: Reliable RST (1)
RST in TCP is unreliable: NIDS may have inconsistent connection state!
  To limit state, NIDS needs to collect state after connection tear down
  Inconsistent state may lead to NIDS evasion
Approach: after RST, send ACK (TCP keep-alive packet)
  If other party missed RST, will return ACK keep-alive packet, otherwise responds with RST

## Slide 48: Reliable RST (2)
Outcomes
  B got RST, replies RST
  B did not get RST, B got ACK, replies ACK
  B did not get RST or ACK
  Normalizer did not get B’s response
Normalizer action
  If AB: RST, send ACK (only after first)
  After BA: RST, tear down state
If only one end host misbehaves, scheme works

## Slide 49: TCP cold start
Problem: how to figure out if a TCP connection is set up after cold start?
Approach
  Assume internal hosts are trusted, set up state if internal host sends TCP packet
  On external TCP packets, probe internal host to check if connection is alive
    Transform packet into TCP keep-alive (by decrementing ACK and removing data)
    If internal host replies with keep-alive, set up state

## Slide 50: Take away slide
Network intrusion detection system can be an alternative (or a complement) to a firewall
Careful design to only process most important events is needed
Decoupling policy from analysis is important
Protocols inherently ambiguous
  Unclear how end-hosts implement the ambiguous parts
  Can be used to evade NIDS
  Possible solution: Protocol normalization (a.k.a. protocol scrubbing)

## Slide 51: Next class: Projects
No need for any reviews 